## Slide 1: Hardware Part 2
Processing Device and Storage Devices

## Slide 2: Processing Characteristics and Functions (continued)
Clock speed: series of electronic pulses produced at a predetermined rate that affects machine cycle time
  Often measured in:
    Megahertz (MHz): millions of cycles per second
    Gigahertz (GHz): billions of cycles per second
Microcode: predefined, elementary circuits and logical operations that the processor performs when it executes an instruction

## Slide 3: Processing Characteristics and Functions
Computer execute an instruction during a machine cycle
Completing the instruction and execution phase – make up one machine cycle
Machine cycle time is measured in:
  Nanoseconds (1 billionth of a second)
  Picoseconds (1 trillionth of a second)
  MIPS (millions of instructions per second)

## Slide 4: Physical Characteristics of the CPU (continued)
Figure 1: Moore’s Law

## Slide 5: Physical Characteristics of the CPU
Collection of digital circuits on chips
Electrical current flows through silicon – to turn the digital circuit on or off
Gordon Moore – former Intel’s chairman hypothesised that progress in chip manufacturing: transistor density of chips will double every 18 months (Moore’s Law)

## Slide 6: Memory Characteristics and Functions
Main memory
  Located physically close to the CPU, but not on the CPU chip itself
  Rapidly provides data and instructions to the CPU

## Slide 7: Storage Capacity
Table 1: Computer Storage Units

## Slide 8: Types of Memory
Figure 2: Basic Types of Memory Chips

## Slide 9: Types of Memory (Cash Memory)
Figure 3: Cache Memory

## Slide 10: Multiprocessing
Multiprocessing: simultaneous execution of two or more instructions at the same time
Multiprocessing using coprocessors
  Coprocessor: speeds processing by executing specific types of instructions while the CPU works on another processing activity

## Slide 11: Parallel Computing
Parallel computing: simultaneous execution of the same task on multiple processors to obtain results faster
Massively parallel processing:
  Speeds processing by linking hundreds or thousands of processors to operate at the same time, or in parallel
  Each processor has its own bus, memory, disks, copy of the operating system, and applications

## Slide 12: Parallel Computing (continued)
2 different approaches to achieving parallel computing
  Single instruction/multiple data (SIMD) parallel processors
  Multiple instruction/multiple data (MIMD) parallel processors
Grid computing: use of a collection of computers, often owned by multiple individuals or organizations, to work in a coordinated manner to solve a common problem

## Slide 13: Secondary Storage
Permanent storage
Compared with memory, offers the advantages of nonvolatility, greater capacity, and greater economy
Selection of secondary storage : access methods, storage capacities, and portability required - determined by the information system’s objectives
Example: credit card company

## Slide 14: Access Methods
Two types of access methods
Sequential access: records must be retrieved in order in which it’s stored
  Devices used are called sequential access storage devices (SASDs)
Direct access: records can be retrieved in any order
  Devices used are called direct access storage devices (DASDs)

## Slide 15: Devices
Magnetic tapes
Magnetic disks
Optical disks
Digital video disk (DVD)
Holographic Versatile Disc (HVD)
Memory cards
Flash memory
RAID
Virtual tape

## Slide 16: Magnetic Tapes
Sequential secondary storage medium
Primarily for storing backups
Tapes similar to audio and videocassettes
Portion of tapes are magnetized to represent bits

## Slide 17: Magnetic Disks
Direct access storage medium
e.g. diskette, hard disks
Allows fast data retrieval

## Slide 18: Optical Disc
Data is recorded by special lasers that physically burn pits in the disk.
Data accessed – optical disc device (compact disk player)
e.g. CD-ROM – 740MB, CD-RW

## Slide 19: DVD and HVD
DVD (Digital Video Disc)
  Looks like a CD but more storage capacity ~ 135min of digital video.
  Software, video games, movies
HVD (Holographic Versatile Disc)
  Advanced optical disk – ongoing research
  Hold 200GB of data
  Write data 10 times faster than DVD

## Slide 20: Memory cards
Functions as a hard disk drive
Portable, relatively easy to use
Need to use memory card reader/writer

## Slide 21: Flash Memory
A silicon computer chip
Keeps its memory when the power is shut off
“Flash” – the memory cell is erased or reprogrammed in a single action or flash
e.g. – Migo – keychain device, comes with software that captures files and settings from e-mail, word processing, web browser, presentation programs.

## Slide 22: RAID and Virtual Tape
Storage technologies
RAID –
  Redundant array of independent /inexpensive disks
  duplicate existing data on drives, provides exact copy, store on different physical disk drives
Virtual Tape
  manages less frequently needed data
  Move data to less costly storage media
  Software – virtual tape server
  Vendor – IBM and Storage Technology

## Slide 23: Enterprise Storage Options
Needs to store massive amount of data
3 forms:
  Attached storage
    tape, hard disks, optical devices
    Simple, cost effective - single users and small groups
    Not allowed share storage
  Network-attached storage (NAS)
    Storage devices attach to a network
    Users can share and access same information

## Slide 24: Enterprise Storage Options (continued)
Figure 3.9: Storage Area Network (SAN)
Storage area network (SAN)
  Special purpose, high speed network
  Provides direct connections between data-storage devices and computer
  Integrates different types of storage subsystems