## Slide 1: Computer Network Introduction

## Slide 2
What is a Network?
A network consists of 2 or more computers connected together, and they can communicate and share resources (e.g. information)

## Slide 3
Why Networking?
Sharing information — i.e. data communication
Do you prefer these?
Or this?

## Slide 4
Sharing hardware or software
Centralize administration and support
E.g. print document
E.g. Internet-based, so everyone can access the same administrative or support application from their PCs

## Slide 5
How many kinds of Networks?
Depending on one’s perspective, we can classify networks in different ways
  Based on transmission media: Wired (UTP, coaxial cables, fiber-optic cables) and Wireless
  Based on network size: LAN and WAN (and MAN)
  Based on management method: Peer-to-peer and Client/Server
  Based on topology (connectivity): Bus, Star, Ring …
  :
  :

## Slide 6
Two main categories:
  Guided ― wires, cables
  Unguided ― wireless transmission, e.g. radio, microwave, infrared, sound, sonar
We will concentrate on guided media here:
  Twisted-Pair cables:
    Unshielded Twisted-Pair (UTP) cables
    Shielded Twisted-Pair (STP) cables
  Coaxial cables
  Fiber-optic cables
Transmission Media

## Slide 7
If the pair of wires are not twisted, electromagnetic noises from, e.g., motors, will affect the closer wire more than the further one, thereby causing errors
Twisted-Pair Cables

## Slide 8
Unshielded Twisted-Pair (UTP)
Typically wrapped inside a plastic cover (for mechanical protection)
A sample UTP cable with 5 unshielded twisted pairs of wires
Metal
Insulator

## Slide 9
Shielded Twisted-Pair (STP)
STP cables are similar to UTP cables, except there is a metal foil or braided-metal-mesh cover that encases each pair of insulated wires

## Slide 10
Categories of UTP Cables
EIA classifies UTP cables according to the quality:
Category 1 ― the lowest quality, only good for voice, mainly found in very old buildings, not recommended now
Category 2 ― good for voice and low data rates (up to 4Mbps for low-speed token ring networks)
Category 3 ― at least 3 twists per foot, for up to 10 Mbps (common in phone networks in residential buildings)
Category 4 ― up to 16 Mbps (mainly for token rings)
Category 5 (or 5e) ― up to 100 Mbps (common for networks targeted for high-speed data communications)
Category 6 ― more twists than Cat 5, up to 1 Gbps

## Slide 11
Coaxial Cables
In general, coaxial cables, or coax, carry signals of higher freq (100KHz–500MHz) than UTP cables
Outer metallic wrapping serves both as a shield against noise and as the second conductor that completes the circuit

## Slide 12
Fiber-Optic Cables
Light travels at 3108 ms-1 in free space and is the fastest possible speed in the Universe
Light slows down in denser media, e.g. glass
Refraction occurs at interface, with light bending away from the normal when it enters a less dense medium
Beyond the critical angle  total internal reflection

## Slide 13
An optical fiber consists of a core (denser material) and a cladding (less dense material)
Simplest one is a multimode step-index optical fiber
Multimode = multiple paths, whereas step-index = refractive index follows a step-function profile (i.e. an abrupt change of refractive index between the core and the cladding)
Light bounces back and forth along the core
Common light sources: LEDs and lasers

## Slide 14
Advantages and Disadvantages
Noise resistance ― external light is blocked by outer jacket
Less signal attenuation ― a signal can run for miles without regeneration (currently, the lowest measured loss is about ~4% or 0.16dB per km)
Higher bandwidth ― currently, limits on data rates come from the signal generation/reception technology, not the fiber itself
Cost ― Optical fibers are expensive
Installation/maintenance ― any crack in the core will degrade the signal, and all connections must be perfectly aligned

## Slide 15
LAN and WAN
Local Area Network (LAN)
  Small network, short distance
    A room, a floor, a building
    Limited by no. of computers and distance covered
    Usually one kind of technology throughout the LAN
    Serve a department within an organization
  Examples:
    Network inside the Student Computer Room
    Network inside CF502
    Network inside your home

## Slide 16
Wide Area Network (WAN)
  A network that uses long-range telecommunication links to connect 2 or more LANs/computers housed in different places far apart.
    Towns, states, countries
  Examples:
    Network of our Campus
    Internet
WAN
Student Computer Centre
Your home
USA

## Slide 17
Example WAN technologies:
  ISDN – Integrated Service Digital Network
    Basic rate: 192 Kbps Primary rate: 1.544Mbps
  T-Carriers ― basically digital phone lines
    T1: 1.544Mbps T3: 28T1
  Frame relay
    Each link offers 1.544Mbps or even higher
  ATM – Asynchronous Transfer Mode
    Support B-ISDN: 155Mbps or 622Mbps or higher
  SONET – Synchronous Optical Network
    Basic rate OC1: 51.84Mbps
    Support OC12 and up to OC192 (9953.28Mbps) or even higher in the future

## Slide 18
Example of WAN: Broadband Cable Network
Cable TV services have been extensively developed in most modern cities
Cable TV companies try to make use of their coaxial cable installed (that are supposed to carry TV signals) to deliver broadband data services
Many cable network wiring has been replaced with hybrid fiber-coax (HFC) ― i.e. use of fiber-optic cable to connect to the subscribers’ buildings, and then the original coaxial cable to connect to each household

## Slide 19
The connection is shared by a number of subscribers, hence may raise performance and security problems
Fiber-optic cable
Cable company
Coaxial
Cable
TV
PC
Cable Drop

## Slide 20
Cable is an asymmetrical technology
  Downstream: max 36 Mbps
  Upstream: max 10 Mbps
May be reduced to 3 – 10 Mbps downstream and 2 Mbps upstream, depending on no. of subscribers
Need a special cable modem
Ethernet
link to PC
Coaxial link
from cable TV
socket
Teryon Cable Modem

## Slide 21
Peer-to-Peer Networks
Peer-to-peer network is also called workgroup
No hierarchy among computers  all are equal
No administrator responsible for the network
Peer-to-peer

## Slide 22
Advantages of peer-to-peer networks:
  Low cost
  Simple to configure
  User has full accessibility of the computer
Disadvantages of peer-to-peer networks:
  May have duplication in resources
  Difficult to uphold security policy
  Difficult to handle uneven loading
Where peer-to-peer network is appropriate:
  10 or less users
  No specialized services required
  Security is not an issue
  Only limited growth in the foreseeable future

## Slide 23
Clients and Servers
  Network Clients (Workstation)
    Computers that request network resources or services
  Network Servers
    Computers that manage and provide network resources and services to clients
      Usually have more processing power, memory and hard disk space than clients
      Run Network Operating System that can manage not only data, but also users, groups, security, and applications on the network
      Servers often have a more stringent requirement on its performance and reliability

## Slide 24
Advantages of client/server networks
  Facilitate resource sharing – centrally administrate and control
  Facilitate system backup and improve fault tolerance
  Enhance security – only administrator can have access to Server
  Support more users – difficult to achieve with peer-to-peer networks
Disadvantages of client/server networks
  High cost for Servers
  Need expert to configure the network
  Introduce a single point of failure to the system

## Slide 25
Topology ― 3 basic types
How so many computers are connected together?
  Bus Topology Ring Topology
  Star Topology
Hub

## Slide 26
  Bus Topology
    Simple and low-cost
    A single cable called a trunk (backbone, segment)
    Only one computer can send messages at a time
    Passive topology - computer only listen for, not regenerate data
  Star Topology
    Each computer has a cable connected to a single point
    More cabling, hence higher cost
    All signals transmission through the hub; if down, entire network down
    Depending on the intelligence of hub, two or more computers may send message at the same time

## Slide 27
How to construct a network with Bus / Star Topology?
  Star Topology
  Bus Topology
BNC T-Connector
Coaxial cable
Network Card

## Slide 28
Ring Topology
  Every computer serves as
  a repeater to boost signals
  Typical way to send data:
    Token passing
      only the computer who
      gets the token can send
      data
  Disadvantages
    Difficult to add computers
    More expensive
    If one computer fails, whole network fails
T
T
T
data
T
data
T
data
T
data
T
data
T
data
T
Ack
T
Ack
T
Ack
T
Ack
T

## Slide 29: Internet Connections
Internet backbone A set of high-speed networks that carry Internet traffic
These networks are provided by companies such as AT&T, GTE, and IBM
Internet service provider (ISP) A company that provides other companies or individuals with access to the Internet

## Slide 30: Internet Connections
There are various technologies available that you can use to connect a home computer to the Internet
  A phone modem converts computer data into an analog audio signal for transfer over a telephone line, and then a modem at the destination converts it back again into data
  A digital subscriber line (DSL) uses regular copper phone lines to transfer digital data to and from the phone company’s central office
  A cable modem uses the same line that your cable TV signals come in on to transfer the data back and forth

## Slide 31: Internet Connections
Broadband A connection in which transfer speeds are faster than 128 bits per second
  DSL connections and cable modems are broadband connections
  The speed for downloads (getting data from the Internet to your home computer) may not be the same as uploads (sending data from your home computer to the Internet)

## Slide 32: Packet Switching
To improve the efficiency of transferring information over a shared communication line, messages are divided into fixed-sized, numbered packets
Network devices called routers are used to direct packets between networks
Figure 15.4 Messages sent by packet switching
15-18

## Slide 33: Open Systems
Proprietary system A system that uses technologies kept private by a particular commercial vendor
  One system couldn’t communicate with another, leading to the need for
Interoperability The ability of software and hardware on multiple machines and from multiple commercial vendors to communicate
  Leading to
Open systems Systems based on a common model of network architecture and a suite of protocols used in its implementation

## Slide 34: Open Systems
The International Organization for Standardization (ISO) established the Open Systems Interconnection (OSI) Reference Model
Each layer deals with a particular aspect of network communication
Figure 15.5 The layers of the OSI Reference Model

## Slide 35: Network Protocols
Network protocols are layered such that each one relies on the protocols that underlie it
Sometimes referred to as a protocol stack
Figure 15.6 Layering of key network protocols

## Slide 36: TCP/IP
TCP stands for Transmission Control Protocol
  TCP software breaks messages into packets, hands them off to the IP software for delivery, and then orders and reassembles the packets at their destination
IP stands for Internet Protocol
  IP software deals with the routing of packets through the maze of interconnected networks to their final destination

## Slide 37: TCP/IP (cont.)
UDP stands for User Datagram Protocol
  It is an alternative to TCP
  The main difference is that TCP is highly reliable, at the cost of decreased performance, while UDP is less reliable, but generally faster

## Slide 38: High-Level Protocols
Other protocols build on the foundation established by the TCP/IP protocol suite
  Simple Mail Transfer Protocol (SMTP)
  File Transfer Protocol (FTP)
  Telnet
  Hyper Text Transfer Protocol (http)

## Slide 39: MIME Types
Related to the idea of network protocols and standardization is the concept of a file’s MIME type
  MIME stands for Multipurpose Internet Mail Extension
  Based on a document’s MIME type, an application program can decide how to deal with the data it is given

## Slide 40: MIME Types
Figure 15.7 Some protocols and the ports they use

## Slide 41: Firewalls
Firewall A machine and its software that serve as a special gateway to a network, protecting it from inappropriate access
  Filters the network traffic that comes in, checking the validity of the messages as much as possible and perhaps denying some messages altogether
  Enforces an organization’s access control policy

## Slide 42: Firewalls
Figure 15.8 A firewall protecting a LAN

## Slide 43: Network Addresses
Hostname A unique identification that specifies a particular computer on the Internet
For example
  matisse.csc.villanova.edu
  condor.develocorp.com

## Slide 44: Network Addresses
Network software translates a hostname into its corresponding IP address
For example
  205.39.145.18

## Slide 45: Network Addresses
An IP address can be split into
  network address, which specifies a specific network
  host number, which specifies a particular machine in that network
Figure 15.9 An IP address is stored in four bytes

## Slide 46: Domain Name System
A hostname consists of the computer name followed by the domain name
csc.villanova.edu is the domain name
  A domain name is separated into two or more sections that specify the organization, and possibly a subset of an organization, of which the computer is a part
  Two organizations can have a computer named the same thing because the domain name makes it clear which one is being referred to

## Slide 47: Domain Name System
The very last section of the domain is called its top-level domain (TLD) name
Figure 15.10 Top-level domains, including some relatively new ones

## Slide 48: Domain Name System
Organizations based in countries other than the United States use a top-level domain that corresponds to their two-letter country codes
Figure 15.11 Some of the top-level domain names based on country codes

## Slide 49: Domain Name System
The domain name system (DNS) is chiefly used to translate hostnames into numeric IP addresses
  DNS is an example of a distributed database
  If that server can resolve the hostname, it does so
  If not, that server asks another domain name server

## Slide 50: Packets
A small chunk of data transmitted over the Internet
Alice
The Internet
Bob

## Slide 51: VPN (Virtual Private Network)
A secure tunnel to a private network through a public network
Once established, local node appears to be a node in the private network in a secure manner
Correction from the book (pg. 11):
  VPN does not mean using telephone line connection!!!

## Slide 52: Host & IP Address
Correction from the book:
  “A host is a computer connected directly to the Internet”
  “You home computer is not a host”
Each host needs an IP address
IP address
  A 32-bit number, arranged in 4 numbers seperated by “.”
  Eg. 74.125.19.147

## Slide 53: DNS (Domain Name System)
Domain name to IP address conversion
  Eg. www.google.com → ??.???.??.??
Domain name or IP address lookup
  http://cqcounter.com/whois/

## Slide 54: Top-level Domains
gTLDs (generic TLDs)
  .com, .edu, .net, .org, .gov, .mil
  .aero, .biz, .coop, .info, .museum, .name, .pro
ccTLDs (country code TLDs)
  .au, .ca, .br, .de, .fi, .fr, .jp, .hk, .cn, .tw, .my, …
  .us

## Slide 55: Second-level Domains
Domains that are directly below a TLD
Eg.
  ucr.edu
  google.com
  sony.co.jp
Must apply to a registrar for the appropriate TLD

## Slide 56: Domain Names & Registrars
Profitable domain names
  CreditCards.com - $2.75M
  Loans.com – $3M
  Business.com - $7.5M
Network Solutions, Inc used to monopolize the name registration
Now, ~500 registrars

## Slide 57: How To Register A Domain Name?
Come up a new name
2 name servers’ IP addresses
1 administrative contact
1 technical contact
Register the name to an Internet domain registrar
  Eg. www.netsol.com, www.godaddy.com
Used to be done via email or fax, now all web-based!

## Slide 58: Policies
AUP (Acceptable Use Policies)
  A legal document, written to protect the ISP from unlawful use of its service, and outlines prohibited uses of the service and possible consequences of misuse
Privacy Policies
  A document describes an ISP’s policy for protecting users’ information

## Slide 59
THANK YOU