## Slide 1: CAPACITY PLANNING
BCM524 – CONSTRUCTION SYSTEM ANALYSIS

## Slide 2: Capacity Planning
Capacity is the ability to hold, receive, store or accommodate raw materials, finished products, customers, etc.
Capacity is the upper limit or ceiling on the load that an operating unit can handle.
Capacity refers to a system’s potential for producing goods or delivering services over a specified time interval
The basic questions in capacity handling are:
  What kind of capacity is needed?
  How much is needed?
  When is it needed?

## Slide 3: Strategic Capacity Planning
Strategic Capacity Planning is an approach for determining the overall capacity level of capital intensive resources, including facilities, equipment and overall labour force size.
Capacity used is the rate of output actually achieved
The best operating level is nominally the capacity of which the process was designed

## Slide 4: Process Selection and System Design
Forecasting
Product and Service Design
Technological Change
Capacity Planning
Process Selection
Facilities and Equipment
Layout
Work Design

## Slide 5: Importance of Capacity Decisions
Impacts ability to meet future demands
Affects operating costs
Major determinant of initial costs
Involves long-term commitment
Affects competitiveness
Affects ease of management
Globalization adds complexity
Impacts long range planning
Notes: Impacts ability to meet future demand for products and services; capability essentially limits the rate of output possible. Having capacity to satisfy demand can allow a company to take advantage of tremendous opportunities.
Affecting operating costs. Ideally, capacity and demand requirements will be matched, which will tend to minimize operating costs. In practice, this is not always achieved because actual demand either differs from expected demand or tends to vary (e.g. Cyclically). In such cases, a decision might be made to attempt to balance the cost of over and under capacity

## Slide 6: Capacity Decisions
Design capacity
  Maximum capability to produce:
    Rated capacity is theoretical
    Effective capacity includes efficiency and utilization
  maximum output rate or service capacity an operation, process, or facility is designed for
Effective capacity
  Design capacity minus allowances such as personal time, maintenance, and scrap
Actual output
  rate of output actually achieved--cannot exceed effective capacity.

## Slide 7: What is capacity?
Capacity Utilization
  Percent of available time spent working
Capacity Efficiency
  How well a machine or worker performs compared to a standard output level
Capacity Load
  Standard hours of work assigned to a facility
Capacity Load Percent
  Ratio of load to capacity

## Slide 8: Capacity Requirement
Dimension of Demand | Effect on capacity requirement
Quantity | How much capacity is needed?
Timing | When should capacity be available?
Quality | What kind of capacity is needed?
Location | Where should capacity be installed?

## Slide 9: Capacity Planning
Capacity is the maximum output rate of a production or service facility
Capacity planning is the process of establishing the output rate that may be needed at a facility :
  Capacity is usually purchased in ‘chunks’
  Strategic issues : how much and when to spend capital additional facility & equipment
  Tactical issues : workforce & inventory levels, and day-to-day use of equipment

## Slide 10: Measuring Capacity Examples
There is no one best way to measure capacity
Output measures like cars per day are easier to understand
While multiple products, inputs measures work better
Type of Business | Input measures of capacity | Output measures of capacity
Car Manufacturer | Labour Hours | Cars per shift
Hospital | Available Beds | Patients per month
Pizza Parlor | Labour Hours | Pizzas per day
Retail Store | Floor Space in ft² | Revenue per ft²

## Slide 11: Efficiency and Utilization
Actual output
Capacity Efficiency =
Effective capacity
Actual output
Capacity Utilization =
Design capacity
Both measures expressed as percentages

## Slide 12: Efficiency/Utilization Example
Actual output = 36 units/day
Efficiency = = 90%
Effective capacity 40 units/ day
Utilization = Actual output = 36 units/day
= 72% Design capacity 50 units/day
Design capacity = 50 trucks/day
Effective capacity = 40 trucks/day
Actual output = 36 units/day

## Slide 13: Determinants of Effective Capacity
Facilities
Product and service factors
Process factors
Human factors
Operational factors
Supply chain factors
External factors
Notes: Facilities - The design of facilities, including size and provision for expansion, is key. Location factors, such as transportation costs, distance to market, labor supply, energy sources, and room for expansion, are also important. Likewise, layout of the work area often determines how smoothly work can be performed, and environmental factors such as heating, lighting and ventilation also play a significant role in determining whether personnel can perform effectively or whether they must struggle to overcome poor design characteristics.
Products and Service Factors - Products or service design can have a tremendous influence on capacity. For example, when items are similar, the ability of the system to produce those items is generally much greater than successive items differ. Thus, a restaurant that offers a limited menu can usually prepare and serve meals at faster rate than a restaurant with an extensive menu.
Process Factors – The quantity capability of a process is an obvious determinant of capacity. A more subtle determinants is the influence of output quality. For instance, if quality of output does not meet standards, the rate of output will be slowed by the need for inspection and rework activities
Human factors - The tasks that make up a job, the variety of activities involved, an the training, skill and experience required to perform a job all have an impact on potential and actual output. In addition, employee motivation has a very basic relationship to capacity, as do absenteeism and labor turnover
Operational factors – Scheduling problems may occur when an organisation has differences in equipment capabilities among alternative pieces of equipment or differences in job requirement. Inventory stocking decisions, late deliveries, purchasing requirements, acceptability of purchased materials and parts and quality inspection and control procedures also can have impact on effective capacity. Insufficient capacity in one area can affect overall capacity.
Supply chain factors – Supply chain factors must be taken into account in capacity planning if substantial capacity changes are involved
External factors – Product standards, especially minimum quality and performance standards can restrict management’s options for increasing and using capacity.

## Slide 14: Table – Factors that determine effective capacity
Facilities
  Design
  Location
  Layout
  Environment
Product / Service
  Design
  Product or service mix
Process
  Quantities capabilities
  Quality Capabilities
Human factors
  Job content
  Job design
  Training and experience
  Motivation
  Compensation
  Learning rates
  Absenteeism and labor turnover
Operational
  Scheduling
  Materials management
  Quality assurance
  Maintenance policies
  Equipment breakdowns
External factors
  Product standards
  Safety regulations
  Unions
  Pollution control standards

## Slide 15: Strategy Formulation
Capacity strategy for long-term demand
Demand patterns
Growth rate and variability
Facilities
  Cost of building and operating
Technological changes
  Rate and direction of technology changes
Behavior of competitors
Availability of capital and other inputs

## Slide 16: Key Decisions of Capacity Planning
Amount of capacity needed
  Involves consideration of expected demand and capacity costs. The greater demand of uncertainty, the greater amount of capacity cushion
Timing of changes
  Relates to availability of capital, lead time needed to make changes and expected demand
Need to maintain balance
  Requires proportionate changes in capacity in all related areas of the system
Extent of flexibility of facilities
  Influence by the uncertainty about demand and the degree of variety in work requirements.
Capacity cushion – extra demand intended to offset uncertainty

## Slide 17: Steps for Capacity Planning
Estimate future capacity requirements
Evaluate existing capacity
Identify alternatives
Conduct financial analysis
Assess key qualitative issues
Select one alternative
Implement alternative chosen
Monitor results

## Slide 18: Calculating Processing Requirements
A department works one eight-hour shift, 250 days a year. And has these figures for usage of a machine that is being considered:
Annual capacity - 8 hours shift and 250 working days a year to produce 3 products – need how many machine?
5,800 hours = 2.9 machines (equiv. To 3 machines)
2,000 hours/machine

## Slide 19: Make or Buy
Available capacity
Expertise
Quality considerations
Nature of demand
Cost
Risk
Once capacity requirements have been determined, the organisation must decide whether to produce a good or provide a service itself, or to outsource (buy) from other organisation. Reason to make or buy as those factors :

## Slide 20: Developing Capacity Alternatives
Design flexibility into systems
Take stage of life cycle into account
Take a “big picture” approach to capacity changes
Prepare to deal with capacity “chunks”
Attempt to smooth out capacity requirements
Identify the optimal operating level

## Slide 21: Economies of Scale
Economies of scale
  If the output rate is less than the optimal level, increasing output rate results in decreasing average unit costs
Diseconomies of scale
  If the output rate is more than the optimal level, increasing the output rate results in increasing average unit costs

## Slide 22: Evaluating Alternatives
Minimum
cost
Average cost per unit
0
Rate of output
Production units have an optimal rate of output for minimal cost.
Minimum average cost per unit
Under- Utilization
Over- Utilization
Best Operating Level

## Slide 23: Evaluating Alternatives
Minimum cost & optimal operating rate are
functions of size of production unit.
Average cost per unit
0
Small
plant
Medium
plant
Large
plant
Output rate

## Slide 24: Planning Service Capacity
Need to be near customers
  Capacity and location are closely tied
Inability to store services
  Capacity must be matched with timing of demand
Degree of volatility of demand
  Peak demand periods

## Slide 25: Evaluating Alternatives
A number of techniques are useful for evaluating capacity alternatives from an economic standpoint.
Some of the more common are cost-volume analysis, financial analysis, decision theory and waiting-line analysis,

## Slide 26: Cost-Volume Analysis
Cost-volume analysis focuses on relationship between cost, revenue and volume of out-put.
The purpose of cost-volume analysis is to estimate the income of an organisation under different operating conditions.
As a tool for comparing capacity alternatives
Fixed costs – remain constant regardless of volume of output (e.g. Rental costs, property taxes, equipment costs, heating and cooling expenses and administrative costs)

## Slide 27: Cost-Volume Analysis
Variable costs – variable costs per unit remains the same regardless of volume of output and all the output can be sold (e.g. Materials and labour costs)
Total costs – volume of output is equal to the sum of the fixed cost and the variable cost per unit times volume:
TC = FC + VC
VC = Q x v
TR = R X Q
FC = Fixed cost
VC = Total variable cost
TC = Total cost
TR = Total revenue
R = Revenue per unit
v = Variable cost per unit
Q = Quantity or volume of output

## Slide 28: Cost-Volume Relationships
Amount ($)
0
Q (volume in units)
Total cost (TC) = VC + FC
Total variable cost (VC)
Fixed cost (FC)
Figure 5.5a
A. Fixed, variable and total costs
VC = Q x v

## Slide 29: Cost-Volume Relationships
Amount ($)
Q (volume in units)
0
Total revenue (TR)
B. Total revenue increases linearly with ouput
TR = R X Q

## Slide 30: Cost-Volume Relationships
Amount ($)
Q (volume in units)
0
Break Even Point (BEP) units
Profit
Total revenue
Total cost
Profit (P) = TR – TC
Or
P = Q (R – v) - FC
Loss
FC
QBEP =
R - v

## Slide 31: Assumptions of Cost-Volume Analysis
One product is involved
Everything produced can be sold
Variable cost per unit is the same regardless of volume
Fixed costs do not change with volume
Revenue per unit constant with volume
Revenue per unit exceeds variable cost per unit

## Slide 32: Example 2 – Cost-Volume Analysis
The owner Old-Fashioned Berry Pie, S.Simon, is contemplating adding a new line of pies, which will require leasing new equipment for a monthly payment of $6,000. Variable costs would be $2.00 per pie, and pies would retail for $7.00 each
  How many pies must be sold in order to break even?
  What would the profit (loss) be if 1,000 pies are made and sold in a month?
  How many pies must be sold to realize a profit of $4,000?
  If 2,000 can be sold, and profit target is $5,000, what price should be charged per pie?

## Slide 33: Example 2 - Solution
FC = $ 6,000, VC = $2 per pie, Rev = $7 per pie
FC $6,000
a. QBEP = = = 1,200 pies/month
Rev – VC $7 - $2
b. For Q = 1,000, P = Q (R - v) – FC
= 1,000($7 - $2) - $6,000
= -$1,000 (loss)

## Slide 34: Example 2 - Solution
c. P = $4,000 using the following formula
P + FC $4,000 + $6,000
Q = = = 2,000 pies
R - v $7 - $2
d. Profit = Q (R - v) - FC
$5,000 = 2,000 (R - $2) - $6,000
R = $ 7.50

## Slide 35: Example 3 – Cost-Volume Analysis
A manager has the opinion of purchasing one, two or three machines. Fixed costs and potential volumes are as follows :
Number of Machines | Total Annual Fixed Costs | Corresponding Range of Output
1 | $9,600 | 0 to 300
2 | $15,000 | 301 to 600
3 | $20,000 | 601 - 900
Variable cost is $10 per unit, and revenue is $40 per unit.
Determine the break-even point for each range.
If projected annual demand is between 580 and 660 units, how many machines should the manager purchase?

## Slide 36: Example 3 - Solution
a. Compute the break-even point for each range using the formula
For 1 machine :
$9,600
QBEP = = 320 units (not in range, so no BEP)
$40/unit - $10/unit
For 2 machines :
$15,000
QBEP = = 500 units
$40/unit - $10/unit
FC
QBEP =
R - v

## Slide 37: Example 3 – Solution (cont’d)
For 3 machines :
$20,000
QBEP = = 666.67 units
$40/unit - $10/unit
b. For projected demand between 580 – 600 units, it is will economic to use 2 machines which the QBEP is 500 units and thus yield a profit.

## Slide 38: Break-Even Problem with Step Fixed Costs
Quantity
FC + VC = TC
FC + VC = TC
FC + VC = TC
Step fixed costs and variable costs.
1 machine
2 machines
3 machines
Figure 5.6a

## Slide 39: Break-Even Problem with Step Fixed Costs
$
TC
TC
TC
BEP
2
BEP
3
TR
Quantity
1
2
3
Multiple break-even points
Figure 5.6b

## Slide 40: Financial Analysis
Cash Flow - the difference between cash received from sales and other sources, and cash outflow for labor, material, overhead, and taxes.
Present Value - the sum, in current value, of all future cash flows of an investment proposal. (e.g Future Value, Internal Rate of Return (IRR) etc.)

## Slide 41: CONCLUSION
Capacity planning involves long-term and short-term considerations
Long –term considerations relate to the overall level of capacity and relate with forecasting
Short-term considerations relate to variable in capacity requirements due to seasonal, random and irregular fluctuations in demand.
Ideally, capacity will match demand

## Slide 42: Exercise
A producer of felt-tip pens received a forecast of demand of 30,000 pens for the coming month from it marketing department. Fixed cost of $25,000/month are allocated to the felt-tip operation, and variable cost are 37 cents per pen.
Find the break-even quantity if pens sell for $1 each
At what price must pens be sold to obtain a monthly profit of $15,000.
Notes: Answer
39683 units
$1.70

## Slide 43
A manager must decide which type of equipment to buy, Type A or Type B. Type A equipment costs $15,000 each and Type B costs $11,000 each. The equipment can be operated 8 hours per day, 250 days a year.
Either machine can be used to perform two types of chemical analysis, C1 and C2. Annual service requirements and processing times are shown in the following table. Which type of equipment should be purchased, and how many of that type will be needed. The goal is to minimise total purchase cost
Total processing time (annual volume x processing time per analysis needed by type of equipment
Analysis Type | Annual Volume | Processing Time (Hr) - A | Processing Time (Hr) – B
C1 | 1,200 | 1 | 2
C2 | 900 | 3 | 2

## Slide 44
A manager must decide which type of machine to buy A, B or C Machine costs A- $40,000, B costs - $ 30,000 and C - $80,000. Product forecast and processing times on the machine are as follows ;
Assume that only purchasing costs are being considered . Which machine have the lowest total cost and how many machine need. Machine operate 10 hours a day, 250 days a year
Machine A have hourly operating costs of $10 each, Machine B $11 each, Machine C $12 each. Which machine can be selected and how many machine need to minimize total cost while satisfying capacity processing requirement.
product | Annual demand | Time processing (min) A | Time processing (min) B | Time processing (min) C
1 | 16000 | 3 | 4 | 2
2 | 12000 | 4 | 4 | 3
3 | 6000 | 5 | 6 | 4
4 | 30000 | 2 | 2 | 1