## Slide 1: Error Detection and Correction
Komunikasi Data

## Slide 2: Objective
Mahasiswa mampu mengenali eror yang terjadi pada transmisi asinkron, dan mendeteksinya dengan menggunakan bit parity.
Mahasiswa mampu mengenali eror yang terjadi pada transmisi sinkron, dan eror dikoreksi dengan menggunakan LRC dan VRC.
Mahasiswa dapat menjelaskan bagaimana mendeteksi eror pada transmisi sinkron dan dengan menggunakan checksum dan CRC
Mahasiswa dapat menjelaskan bagaimana eror pada transmisi sinkron dapat dikoreksi dengan menggunakan kode Hamming
Mahasiswa mampu menjelaskan bagaimana eror dapat dikoreksi menggunakan ARQ (Automatic Repeat Request).

## Slide 3: Error Detection and Correction
1 Types of Errors
2 Detection
3 Error Correction

## Slide 4: Error Detection and Correction
Data can be corrupted during transmission. For reliable communication, error must be detected and corrected
are implemented either at the data link layer or the transport layer of the OSI model

## Slide 5: 1. Type of Errors

## Slide 6: Type of Errors(cont’d)
Single-Bit Error
~ is when only one bit in the data unit has changed (ex : ASCII STX - ASCII LF)

## Slide 7: Type of Errors(cont’d)
Multiple-Bit Error
~ is when two or more nonconsecutive bits in the data unit have changed(ex : ASCII B - ASCII LF)

## Slide 8: Type of Errors(cont’d)
Burst Error
~ means that two or more consecutive bits in the data unit have changed

## Slide 9: 2. Detection
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination

## Slide 10: Detection(cont’d)
Redundancy

## Slide 11: Detection(cont’d)
Detection methods
  VRC (Vertical Redundancy Check)
  LRC (Longitudinal Redundancy)
  CRC (Cyclical redundancy Check)
  Checksum

## Slide 12: Detection(cont’d)
VRC(Vertical Redundancy Check)
  A parity bit is added to every data unit so that the total number of 1s(including the parity bit) becomes even for even-parity check or odd for odd-parity check
  VRC can detect all single-bit errors. It can detect multiple-bit or burst errors only the total number of errors is odd.

## Slide 13: Detection(cont’d)
Even parity VRC concept

## Slide 15: Detection(cont’d)
LRC(Longitudinal Redundancy Check)
  Parity bits of all the positions are assembled into a new data unit, which is added to the end of the data block

## Slide 20: Detection(cont’d)
CRC(Cyclic Redundancy Check)
~ is based on binary division.

## Slide 21: Detection(cont’d)
CRC generator
~ uses modular-2 division.
Binary Division
in a
CRC Generator

## Slide 22: Detection(cont’d)
Binary Division
in a
CRC Checker

## Slide 23: Detection(cont’d)
Polynomials
  CRC generator(divisor) is most often represented not as a string of 1s and 0s, but as an algebraic polynomial.

## Slide 24: Detection(cont’d)
A polynomial representing a divisor

## Slide 25: Detection(cont’d)
Standard polynomials

## Slide 27: Detection(cont’d)
Checksum
~ used by the higher layer protocols
~ is based on the concept of redundancy(VRC, LRC, CRC ….)

## Slide 28: Detection(cont’d)
Checksum Generator

## Slide 29: Detection(cont’d)
To create the checksum the sender does the following:
  The unit is divided into K sections, each of n bits.
  Section 1 and 2 are added together using one’s complement.
  Section 3 is added to the result of the previous step.
  Section 4 is added to the result of the previous step.
  The process repeats until section k is added to the result of the previous step.
  The final result is complemented to make the checksum.

## Slide 31: Detection(cont’d)
data unit and checksum

## Slide 32: Detection(cont’d)

## Slide 33: 3. Error Correction
~ can be handled in two ways
 when an error is discovered, the receiver can have the sender retransmit the entire data unit.
 a receiver can use an error-correcting code, which automatically corrects certain errors.